## Slide 1
QUADRUPED ROBOT DEVELOPMENT
━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━
Certification-Based Industrial Training
WTL & MeitY Project | Group-E
Department of Electronics & Communication Engineering
Cooch Behar Government Engineering College | 2026
Guided by: Dr. Palash Das (ECE) | Mrs. Susmita Banik Barik (Project Eng., WTL) | Mr. Arijit Bhunia | Mr. Bhaskar Mondal

## Slide 2
Team Members — Group E
Department of ECE, CGEC | WTL & MeitY Project | 2026
Quadruped Robot Development | Group-E | ECE Dept., CGEC | WTL & MeitY | 2026
2/21
#
Name
Roll No.
Reg. ID
1
Sarupya Guha
34900323046
FS08A0198
2
Sohan Ghosh
34900323050
FS08A0202
3
Sayan Sarkar
34900323048
FS08A0157
4
Debanjan Chakraborty
34900323015
FS08A0154
5
Joydip Das
34900323020
FS08A0220
6
Aushi Sarkar
34900323011
FS08A0288
7
Anupam Dutta
34900323003
FS08A0206
8
Bikkram Das
34900323012
FS08A0528
9
Biraj Sarkar
34900323013
FS08A0239
GUIDED BY
Dr. Palash Das
ECE
Mrs. Susmita
Banik Barik
Proj. Eng., WTL
Mr. Arijit Bhunia
Proj. Co-ord.
Mr. Bhaskar
Mondal
Faculty, WTL
10
Soumyajit Pandit
34900323052
FS08A0189

## Slide 3
Project Objective
What are we building and why?
Quadruped Robot Development | Group-E | ECE Dept., CGEC | WTL & MeitY | 2026
3/21
▶
Design, fabricate & program a fully functional 8-DOF Quadruped Robot
▶
Use affordable, open-source components and tools (ESP32 + FreeCAD + FDM printing)
▶
Core hardware: ESP32 microcontroller | PCA9685 16-ch servo driver | 9× MG90S servos
▶
Chassis designed in FreeCAD — fabricated with FDM 3D printing (PLA+ & PETG)
▶
Hands-on experience across: Electronics • Mechanical Design • Additive Manufacturing
▶
End goal: Robot capable of standing stably and executing a walking gait
▶
Future roadmap: Sensor integration → Autonomous navigation
▶
Aligned with GoI skills development initiative under WTL & MeitY programme

## Slide 4
Introduction — What is a Quadruped Robot?
Quadruped Robot Development | Group-E | ECE Dept., CGEC | WTL & MeitY | 2026
4/21
▶
A legged mobile robot that moves on four limbs — mimicking dogs, horses, insects
▶
Unlike wheeled robots, quadrupeds navigate uneven terrain, climb stairs, step over obstacles
▶
Each leg has 2+ joints providing degrees of freedom for stable gait generation
▶
This robot: Hip joint + Knee joint per leg → 8 DOF for locomotion + 1 DOF head rotation
▶
Notable examples: Boston Dynamics Spot • Unitree Go1 • University research platforms
8 DOF
Locomotion (4 hips + 4 knees)
1 DOF
Head Rotation
9 Total
MG90S Servos
3 Domains
Electronics Mechanical 3D Printing

## Slide 5
Real-World Applications of Quadruped Robots
Quadruped Robot Development | Group-E | ECE Dept., CGEC | WTL & MeitY | 2026
5/21
🔍 Search & Rescue
Navigates rubble, collapsed structures and disaster zones where wheels cannot go
⚙ Rough Terrain
Pipeline inspection, mining surveys, and remote area monitoring
🎖 Military / Defence
Cargo carrying, reconnaissance missions, and hazardous environment scouting
🏥 Medical / Rehab
Companion and assistive robots for elderly care and rehabilitation
🔬 Research Platform
Studying locomotion algorithms, control theory, and AI-based navigation
🏭 Industrial
Automated factory floor inspection and infrastructure monitoring

## Slide 6
Why ESP32? & Why 3D Printing?
Quadruped Robot Development | Group-E | ECE Dept., CGEC | WTL & MeitY | 2026
6/21
ESP32 — Central Controller
▶
Dual-core 240 MHz processor — powerful yet low-cost
▶
Built-in Wi-Fi & Bluetooth for wireless control
▶
Supports I2C and SPI for peripheral communication
▶
Well-supported Arduino IDE ecosystem
▶
ESP32Servo library — direct servo control via PWM
▶
Wireless capability → OTA updates, remote teleoperation
3D Printing — Chassis Fabrication
▶
Rapid iteration on part dimensions without tooling cost
▶
Customised mounting positions for every component
▶
Fabricate geometrically complex parts cheaply
▶
PLA+ → structural rigidity for Core Plate & Head Box
▶
PETG → flexibility & impact resistance for leg links
▶
Entire robot chassis printed in the CGEC 3D Printing Lab

## Slide 7
Development Roadmap — 9-Phase Journey
From component verification to autonomous navigation
Quadruped Robot Development | Group-E | ECE Dept., CGEC | WTL & MeitY | 2026
7/21
Phase 1
Servo & MCU Test
Complete
›
Phase 2
CAD Design
Complete
›
Phase 3
3D Printing
Complete
›
Phase 4
Assembly
Complete
›
Phase 5
Standing Pose
Complete
›
Phase 6
Walking Gait
In Progress
›
Phase 7
Turning Gait
Planned
›
Phase 8
Sensor Integration
Future
›
Phase 9
Autonomous Nav.
Future
Complete
In Progress / Planned
Future Roadmap
📌 This report covers Phases 1–5 in detail. Phases 6–9 form the future roadmap.

## Slide 8
Electronics Architecture
4-Layer electronics stack
Quadruped Robot Development | Group-E | ECE Dept., CGEC | WTL & MeitY | 2026
8/21
Layer 1 — Central Controller
ESP32 Dev Board (I2C Master, Dual-core 240 MHz)
▼
Layer 2 — Servo Driver
PCA9685 16-Channel PWM Driver (I2C Slave @ 0x40)
▼
Layer 3 — Actuators
9× MG90S Metal Gear Micro Servos (4 Hip + 4 Knee + 1 Head)
▼
Layer 4 — Power Supply
External 5V Supply → PCA9685 V+ Servo Rail
ESP32 → PCA9685 Wiring
ESP32 Pin
PCA9685 Pin
3.3V
VCC
GND
GND
GPIO21
SDA
GPIO22
SCL
⚠ PCA9685 V+ rail MUST have an external 5V supply (separate from VCC)

## Slide 9
Servo Channel Mapping
PCA9685 CH0–CH8 → 9 MG90S servos
Quadruped Robot Development | Group-E | ECE Dept., CGEC | WTL & MeitY | 2026
9/21
CH0
Front Left Hip
Type: Hip
CH1
Front Left Knee
Type: Knee
CH2
Front Right Hip
Type: Hip
CH3
Front Right Knee
Type: Knee
CH4
Rear Left Hip
Type: Hip
CH5
Rear Left Knee
Type: Knee
CH6
Rear Right Hip
Type: Hip
CH7
Rear Right Knee
Type: Knee
CH8
Head Rotation
Type: Head
Hip Servo
Knee Servo
Head Servo

## Slide 10
Critical Discovery — Servo Power Rail Issue
Real-world debugging experience during Phase 1
Quadruped Robot Development | Group-E | ECE Dept., CGEC | WTL & MeitY | 2026
10/21
⚠ SYMPTOM
All 9 servos were completely unresponsive when controlled via PCA9685
🔍 I2C DIAGNOSIS
I2C scanner confirmed PCA9685 at address 0x40 — ESP32, I2C bus, and chip all functioning correctly
🔎 ROOT CAUSE
V+ rail measured only 0.10 V (expected 4.8–5.2 V) — servo power rail NOT connected to external 5V supply
✅ RESOLUTION
Connected 5V directly to PCA9685 V+ terminal → Servos responded immediately. V+ measured 4.92–5.05 V
📖 LESSON
Always verify servo rail voltage FIRST before suspecting firmware or I2C communication issues

## Slide 11
Mechanical Architecture & Component Dimensions
FreeCAD-designed chassis — all parts 3D printed
Quadruped Robot Development | Group-E | ECE Dept., CGEC | WTL & MeitY | 2026
11/21
Structural Overview
▶
Two main assemblies: Head Box (electronics enclosure) + Core Plate (central chassis)
▶
Head Box — houses ESP32, PCA9685, power switch + future sensor mount provision
▶
Core Plate — mounts all 4 hip servos + 1 head servo (5 total on chassis)
▶
Each leg: Upper Leg (hip-driven) + Lower Leg (knee-driven) → 2 links per leg
Component Dimensions
Component
Dimensions (mm)
Notes
Core Plate
110 × 85 × 4
4 hip mounts + 1 head servo
Head Box
85 × 65 × 45
Wall 2.5 mm — ESP32, PCA9685
Upper Leg ×4
45 × 10 × 5
PETG — hip servo driven
Lower Leg ×4
55 × 10 × 5
PETG — knee servo driven
Servo Mount×9
Custom press-fit
PLA+ — MG90S body fit

## Slide 12
FreeCAD Design Workflow
Part Design workbench — parametric modelling
Quadruped Robot Development | Group-E | ECE Dept., CGEC | WTL & MeitY | 2026
12/21
1
Core Plate
Base 110×85×4 mm plate with 4 symmetric hip servo pockets and central head servo mount
2
Head Servo Mount
Centred on Core Plate; controls head rotation via MG90S (CH8)
3
Hip Servo Mounts
Four symmetric press-fit pockets at FL, FR, RL, RR corners
4
Upper Leg
45 mm PLA link with servo horn connection hole at proximal end
5
Lower Leg
55 mm PLA link with foot pad boss at distal (terminal) end
6
Head Box
Enclosure designed around ESP32 and PCA9685 PCB footprints (85×65×45 mm)
7
Assembly
All bodies assembled in FreeCAD Assembly with correct spacing and constraints

## Slide 13
3D Printing Process — FDM Technology
CAD → STL → G-code → Print
Quadruped Robot Development | Group-E | ECE Dept., CGEC | WTL & MeitY | 2026
13/21
Fused Deposition Modelling (FDM): thermoplastic filament melted & deposited layer-by-layer | Workflow: CAD Model → STL Export → Slicer (G-code) → 3D Printer
Material Selection
PLA+
Core Plate, Head Box, Servo Mounts
High stiffness, low warping, easy to print
PETG
Upper Leg, Lower Leg (×4 each)
Toughness & flexibility for repeated bending/impact loads
Slicer Settings
Parameter
Value
Layer Height
0.2 mm
Infill Density
40%
Perimeter Walls
4
Nozzle Diameter
0.4 mm
Print Speed
50 mm/s
Support
As required

## Slide 14
3D Printing in the Lab
Fabrication of quadruped robot components at CGEC 3D Printing Lab
Quadruped Robot Development | Group-E | ECE Dept., CGEC | WTL & MeitY | 2026
14/21
3D Printer (FDM) in the CGEC Lab during fabrication of the Core Plate and Head Box using ABS.
Fabricated leg components (Upper and Lower leg segments) printed in magenta PLA+ for high layer adhesion and impact strength.

## Slide 15
Products Made — 3D Printed Parts
19 total printed components
Quadruped Robot Development | Group-E | ECE Dept., CGEC | WTL & MeitY | 2026
15/21
Part
Material
Dimensions
Qty
Description
Core Plate
ABS
110×85×4 mm
1
Central chassis; 4 hip mounts + 1 head servo mount; 4mm thickness for bending rigidity
Head Box
ABS
85×65×45 mm
1
Electronics enclosure for ESP32, PCA9685 & power switch; 2.5mm walls; future sensor provision
Upper Leg
PLA+
45×10×5 mm
4
Hip-servo driven link; servo horn attachment hole at proximal end
Lower Leg
PLA+
55×10×5 mm
4
Knee-servo driven link; foot pad boss at distal terminal end
Servo Mount
ABS
Custom fit
9
Press-fit housing for MG90S servo body; one per servo

## Slide 16
Arduino Programming
Arduino IDE + ESP32 board support package
Quadruped Robot Development | Group-E | ECE Dept., CGEC | WTL & MeitY | 2026
16/21
Development Environment & Libraries
ESP32Servo
Direct servo control via GPIO PWM
Wire
I2C communication for PCA9685
Adafruit_PWMServoDriver
High-level PCA9685 servo control
Code Listings
Listing 1
Servo Test Code: Direct GPIO18 sweep — 0° → 90° → 180° per servo
Listing 2
PCA9685 I2C Scanner: Scans I2C bus, confirms address 0x40
Listing 3
I2C Scan Output: Expected serial monitor: 'I2C device found at 0x40'
Listing 4
PCA9685 Servo Control: All-channel sweep through Adafruit PWM library
// Servo Test Code — ESP32 direct GPIO18
#include <ESP32Servo.h>
Servo myServo;
void setup() {
myServo.attach(18); // GPIO18
}
void loop() {
myServo.write(0); delay(1000);
myServo.write(90); delay(1000);
myServo.write(180); delay(1000);
}

## Slide 17
Results & Testing
I2C verification · Power rail · All-servo sweep
Quadruped Robot Development | Group-E | ECE Dept., CGEC | WTL & MeitY | 2026
17/21
I2C Communication Verification
PCA9685 confirmed at address 0x40 via I2C scanner
Full chain validated: ESP32 → GPIO21/22 → SDA/SCL → PCA9685
Power Rail Diagnosis & Resolution
Before fix: V+ = 0.10 V (expected 4.8–5.2 V)
After fix: V+ = 4.92–5.05 V → All servos responded immediately
Individual Servo Test Results (All 9 Passed)
#
Function
0°
180°
1
Front Left Hip (CH0)
✓ Pass
✓ Pass
2
Front Left Knee (CH1)
✓ Pass
✓ Pass
3
Front Right Hip (CH2)
✓ Pass
✓ Pass
4
Front Right Knee (CH3)
✓ Pass
✓ Pass
5
Rear Left Hip (CH4)
✓ Pass
✓ Pass
6
Rear Left Knee (CH5)
✓ Pass
✓ Pass
7
Rear Right Hip (CH6)
✓ Pass
✓ Pass
8
Rear Right Knee (CH7)
✓ Pass
✓ Pass
9
Head Rotation (CH8)
✓ Pass
✓ Pass

## Slide 18
Development Phase Status
Current progress across all 9 phases
Quadruped Robot Development | Group-E | ECE Dept., CGEC | WTL & MeitY | 2026
18/21
1
Component Verification
Complete
2
CAD Design in FreeCAD
Complete
3
3D Printing All Parts
Complete
4
Servo Calibration
Complete
5
Standing Pose
Complete
6
Walking Gait
In Progress
7
Turning Gait
Planned
8
Sensor Integration
Planned
9
Autonomous Navigation
Future
55% Complete (5 of 9 Phases)

## Slide 19
Conclusion
Key achievements and future roadmap
Quadruped Robot Development | Group-E | ECE Dept., CGEC | WTL & MeitY | 2026
19/21
Electronics
Systematic debugging validated: I2C chain, servo power rail fix, all 9 servos operational across full 0°–180° range
Mechanical Design
Parametric FreeCAD CAD workflow mastered: servo mounts, press-fit tolerances, STL export → design-for-manufacture skills
3D Printing
Hands-on material selection (PLA+, PETG & ABS), slicer optimization, and print quality assessment in CGEC Lab
Overall Platform
Fully functional 8-DOF quadruped hardware + software stack built — validated foundation for walking gait development
Roadmap: Phase 6 Walking Gait (IK) → Phase 7 Turning → Phase 8 Sensors → Phase 9 Autonomous Navigation via ESP32 Wi-Fi

## Slide 20
References
Quadruped Robot Development | Group-E | ECE Dept., CGEC | WTL & MeitY | 2026
20/21
[1]
Previous Batch Project Report — 3D Printing and Embedded Systems, CGEC Dept. of ECE, WTL & MeitY Project, Cooch Behar, West Bengal, 2024
[2]
Espressif Systems, ESP32 Technical Reference Manual, v5.3, Espressif Systems, 2024
[3]
NXP Semiconductors, PCA9685 16-channel 12-bit PWM I2C-bus LED controller, Product datasheet Rev. 4, NXP, 2015
[4]
Tower Pro, MG90S Metal Gear Micro Servo Datasheet, Tower Pro Co. Ltd., 2020
[5]
FreeCAD Community, FreeCAD: Your Own 3D Parametric Modeler, https://www.freecad.org

## Slide 21
THANK YOU
━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━
Quadruped Robot Development | Group-E | CGEC 2026
WTL & MeitY Industrial Training Programme
Guided by: Dr. Palash Das · Mrs. Susmita Banik Barik · Mr. Arijit Bhunia · Mr. Bhaskar Mondal